## Slide 1: GMA 11 Meeting: Model Recalibration/Limitations (TM 16-01) Summary of Scenario 4 (TM 16-02) Storage Discussion
Bill Hutchison, Ph.D., P.E., P.G.
GMA 11 Meeting
March 22, 2016

## Slide 2: Topics
Technical Memorandum 16-01 (Model Recalibration and Model Limitations)
Technical Memorandum 16-02 (Summary of Scenario 4)
Storage discussion

## Slide 3: Updating Model Calibration
Attempts to update model calibration period did not yield a result that was as good or better than 1975 to 1999 calibration period
Identified limitations of the model that are useful in using Scenario 4 results (or results of any scenario) for development of DFCs
Documented in Technical Memorandum 16-01

## Slide 4: Summary of Effort
9 PEST runs
  Total of 7,610 model runs
2000 to 2013 Recharge and ET based on rainfall relationship
Pumping based on two approaches:
  TWDB estimates for 2000 to 2013
  Use 1999 pumping from model and allow PEST to adjust to improve fit

## Slide 8: Limitations Identified
Problems in outcrop areas
  Use Carrizo as the example
Complex relationship between recharge, ET, discharge to surface water and movement downdip
Storage in outcrop area is increasing from 1975 to 1999 in calibrated model
  Changes in storage are well correlated with recharge

## Slide 16: Discussion
Comparison of 1975-1999 and 2000-2070
  Recharge is the same
  Pumping increases
  Expect decrease in other outflows and increased inflows
ET and Downdip movement increase (not expected)
Appears that water cannot discharge, so storage increases
  ET goes up due to higher heads
  May be related to high specific yield numbers and not enough downdip movement of water

## Slide 17
From Kelley and others (2004)

## Slide 18
From Kelley and others (2004)

## Slide 19
From Kelley and others (2004)

## Slide 20: GMA 11 area
58,269 cells in downdip areas of all aquifers
4,623 cells (8 percent) in 1999 groundwater elevation below the top of the aquifer
  Uses specific yield and not storativity to estimate changes in head
Model may not accurately simulate decreases in groundwater levels due to pumping due to use of higher specific yield value (rather than storativity)
Simulated gradient is flatter than reality – can’t move water from outcrop to downdip
  Storage in outcrop area increases

## Slide 21: Implications for DFC
Note that storage in Scenario 4 is flat (just slightly positive)
Can assume that “negative” drawdowns should be zero for DFC calculations (see TM 16-02)

## Slide 22: Good News
TWDB is expected to update model of Northern Carrizo-Wilcox, Queen City and Sparta
TWDB approved advertising for RFQs for model update (March 21, 2016 TWDB meeting)
  Work is expected to begin later this year
  $800,000 budget
  2 to 3 year completion
New model should be available for next round of joint planning (proposed DFC in spring 2021)

## Slide 23: Topics
Technical Memorandum 16-01 (Model Recalibration and Model Limitations)
Technical Memorandum 16-02 (Summary of Scenario 4)
Storage discussion

## Slide 24: Summary of TM 16-02
Scenario 4 chosen since it met the objectives of GMA 11
  Included previous MAG concepts (i.e. Queen City)
  Included RWP strategies (recommended and alternative)
  Included Forestar project
TM can be viewed as a template
  Tables for a different scenario could be substituted
Objective was to provide a summary suitable for presentation to GCD Boards

## Slide 25: Overview
Table 1 – pumping from Scenario 4
Table 2 – drawdown from Scenario 4 (raw)

## Slide 28: Average Drawdown
Not equal drawdown throughout county
Model cells are 1 square mile
Drawdowns in each cell in a specific county and model layer is summed and then divided by the number of active cells in that county in the model layer
Number of active cells is adjusted to account for dry cells (removed from calculation)
Table 3 has active cells in 2070

## Slide 30: 27 Instances of Negative Drawdown in 2070 in Scenario 4
Table 4 summarizes these occurrences
  County
  Layer
  Drawdown
  Number of Active Cells
  Number of Dry Cells
  Pumping
  Percent of Active Area to Total Area of County in GMA 11

## Slide 32: Observations
16 of the 27 are in areas less than 200 square miles
8 of the 27 are in areas greater than 200 square miles
  One in layer 2 and one in layer 4 (confining units)
  Recommend that DFCs are defined in aquifer units only
Of the six remaining, recommend setting negative drawdowns to zero and recalculating average drawdown
  Model limitation discussed earlier
  San Augustine County – Layer 8 as example

## Slide 34: Summary of Recommendations
Remove layers 2 and 4 (confining units) from DFC consideration
Remove all areas less than 200 square miles (potential monitoring difficulties)
Substitute six instances of negative average drawdown with recalculated average drawdown as described
Panola County GCD will provide their values based on Wade’s work

## Slide 36: Topics
Technical Memorandum 16-01 (Model Recalibration and Model Limitations)
Technical Memorandum 16-02 (Summary of Scenario 4)
Storage discussion

## Slide 37: Storage Discussion
Part of DFC Factor 3
TWDB Report (GAM Task 13-034)
Aquifer | Total Storage (million acre-feet) | Estimated Range of Recoverable Storage (million acre-feet)
Sparta | 55.3 | 13.8 to 41.5
Queen City | 142.0 | 35.5 to 106.5
Carrizo-Wilcox | 2,070.6 | 517.7 to 1,553.0

## Slide 38: Model Limitations and Storage
Issues identified and discussed today suggest that some model parameters used in storage calculations may need updating
How those parameters affect storage calculations already completed by TWDB

## Slide 39: Storage Calculations by TWDB
Three components
  Outcrop area
  Artesian portion of downdip area
  Saturated portion of downdip area

## Slide 40: Outcrop Area
Saturated thickness: 1999 groundwater elevation minus aquifer bottom elevation
Storage = Saturated thickness * Area * Specific Yield
  Area = 640 acres per cell
  Specific yield = 0.1 or 0.15 depending on layer
Carrizo-Wilcox Aquifer Outcrop = 114 million AF

## Slide 41: Artesian Portion of Downdip
Artesian zone thickness: 1999 groundwater elevation minus elevation of top of aquifer
Storage = Artesian zone thickness * Area * Storativity
  Area = 640 acres per cell
  Storativity ranges from 7.3E-05 to 9.93E-03
Carrizo-Wilcox Aquifer Artesian Storage = 65 million AF

## Slide 42: Saturated Portion of Downdip Area
Saturated zone thickness:
  If head below top of aquifer, 1999 groundwater elevation minus elevation of bottom of aquifer
  If head above top of aquifer, elevation of top of aquifer minus elevation of bottom of aquifer
Storage = saturated zone thickness * Area * specific yield
  Area = 640 acres per cell
  Specific yield = 0.1 or 0.15 depending on layer
Carrizo-Wilcox Aquifer Downdip Saturated Storage = 1,879 million AF

## Slide 43: Total Storage
Outcrop = 114 MAF
Downdip (Artesian) = 65 MAF
Downdip (Saturated) = 1,879 MAF
Total = 2,058 MAF
  TWDB Estimate is 2,071 MAF
  Estimate is 2,067 MAF if the correction of downdip areas already below top of aquifer is not made

## Slide 44: Assumption of Specific Yield
MODFLOW requires storativity and specific yield values for each layer (convertible layers)
  If groundwater is above top – storativity is used
  If groundwater is below top – specific yield is used
In most cases, specific yield is never “used” in model calculations for the downdip areas
  23,320 cells of 58,269 total cells in downdip area have artesian head of greater than 500 feet (40 %)
Accuracy of specific yield in the deep saturated zone is not known
  Not part of model calibration

## Slide 45
From Kelley and others (2004)

## Slide 46
From Kelley and others (2004)

## Slide 47
From Kelley and others (2004)

## Slide 48
From Kelley and others (2004)

## Slide 49: What if the Specific Yield was Different?
Specific Yield of 0.1 or 0.15 is representative of clean sand
Interlayered system of sands and clays are common in the Carrizo-Wilcox (well logs)
Model layering has thick layers
  14,107 cells of 58,269 total cells are greater than 500 feet thick (24 percent)
  With thick cells, changes of interbedded clay increases and this would reduce specific yield in these layers
  Higher number is appropriate for the individual sand units, thicker layers increases chance that the overall number would be lower

## Slide 50: Sensitivity of Specific Yield
Minimum storativity is about 0.001
If specific yield in the saturated portion of the downdip area is 0.01 or 0.015 (depending on layer)
  Outcrop area = 114 MAF (unchanged)
  Artesian portion of downdip area = 65 MAF (unchanged)
  Saturated portion of downdip area = 188 MAF
  Total = 367 MAF
    Compare to estimate using actual model parameters of 2,058 MAF

## Slide 51: How Reasonable is Specific Yield Used in the Model
When developed in 2004, doubtful that the developers considered the possibility of using the model to calculate total aquifer storage (place holder parameters)
Problems in outcrop may be due to flat gradients that reduce flow from outcrop to downdip area
Flat gradients can be caused by underestimated drawdown due to pumping or drought conditions
If specific yield in these areas was reduced, gradients might improve conditions to move water into downdip area
Could prevent unrealistic increase in outcrop storage during calibration period of model

## Slide 52: Budget Summary
Task 1 (Initial Simulations)
  Technical Memorandum 15-01 (September 2, 2015)
  Discussion at November 4, 2015 GMA 11 meeting
  Completed for $12,000

## Slide 53: Budget Summary
Task 2 (Update Model Calibration and Rerun Simulations with Updated Pumping)
  Technical Memorandum 16-01 (March 21, 2016)
  Technical Memorandum 16-02 (March 21, 2016)
  Calibration from 2000 to 2013 not as good as 1975 to 1999
  No need to rerun simulations
  No need to fully document model update
  Reduced level of effort
  Budget of $6,000
    Propose revision to $4,000

## Slide 54: Budget Summary
Task 3 (Use model output to address DFC Factors 3 and 4)
  Work completed
  Elements in TM 16-01 and 16-02
  Summarized in today’s PowerPoint (Water Budgets and Storage discussion)
  Recommend expansion and incorporation into Draft Explanatory Report (no separate TM)
  Budget of $5,000
    Propose revision to $4,000

## Slide 55: Budget Summary
Task 1 = $12,000 (Completed)
To be invoiced after today’s meeting = $8,000
  Task 2 = $ 4,000 (Completed – Reduced)
  Task 3 = $ 4,000 (Completed – Reduced)
Total completed to date = $20,000

## Slide 56: Proposed Completion Tasks Prior to April 28, 2016 Meeting
Task 4 - Document Aquifers Not Relevant for Joint Planning
  Proposed Cost = $1,500
Task 5 – Prepare Draft Explanatory Report and attend April 29, 2016 GMA 11 meeting
  Proposed Cost = $8,500

## Slide 57: Other Aquifers in GMA 11
Trinity Aquifer
Nacatoch Aquifer
Yegua-Jackson Aquifer and the Catahoula Formation portion of the Gulf Coast Aquifer System
Gulf Coast Aquifer System

## Slide 58: Overall Budget
Completed Tasks (1, 2, and 3) - $20,000
Proposed Task 4 - $1,500
Proposed Task 5 - $8,500
Total = $30,000

## Slide 59: Questions and Discussion
Bill Hutchison, Ph.D., P.E., P.G.
billhutch@texasgw.com
512-745-0599